## Slide 1: Reduce polygons using Blender

## Slide 2: Import
File > Import > (.obj) or (.3ds) or (.stl)…
[Shift+C] to view the whole of object.
  And center 3d cursor at world origin
[a] to select/deselect all.
  Select[Ctrl+L] to select connected mesh.(edit mode)
[tab] to toggle Object/Edit modes.

## Slide 3: Unit and Geometry
Check the unit of the object.
  The units of object was millimeters.
Resize[s] the object to 1/1000.
  1mm = 0.001BU(1BlenderUnit = 1Meter)
Rotate[r] the object.(+[x,y,z] to lock axis)
  upward = Z axis.
Join[Ctrl+J] all objects and set a origin.

## Slide 4: Reduce Triangles
Find part with excessive detail
  Apply the Modifier ‘Decimate’
  or
  Replace it with some simpler mesh.
  Cylinder uses many triangles.
  Bevels are too smooth.
  Hollows can be filled.

## Slide 5: Base
Subdivide[w] surface and move edges.
Remove[x] the source object.
Duplicate[Shift-D] and Mirror[Ctrl-M] this for the other side.

## Slide 6: Base
Create[Shift-A] a new cube shape.
Move[g] surfaces of the cube.
Subdivide[w] surface and move[g] edges.
Remove[x] the source object.

## Slide 7: Feet
To reduce bevel edges, select mesh[Ctrl-L] then ‘Convert to Quad[Alt-J]’ and dissolve edges[x].
To add some bevels, select edge and press [Ctrl-B].

## Slide 8: Rollers
Reduce the vertex of cylinder.
  Add cylinders and replace.
  (1916tris -> 176tris)x10
Use ‘Array modifier’.
  Count 10
  Set Relative Offset 1.5
1.5

## Slide 9: Model Parts
To make a group of meshes, select mesh and join[Ctrl-J].
To separate mesh, select mesh and press [p].
Use the same name for object and mesh.

## Slide 10: Shading
Change shade setting of mesh
  [w] ‘Shade flat’/’Shade smooth’.
If mesh has 2 or more different shade setting, these are counted as different model parts in Sym3.

## Slide 11: Export as OBJ
File size
  Original - 1680KB
  Reduced - 65KB
-1.6MB